## Slide 1
HELICOPTER
MISSION REQUEST
VADE MECUM
Notes: http://www.easa.europa.eu/ehest/
www.ehest.org
EHEST co-Chairs
Gilles.Bruniaux@airbus.com
John.Vincemt@easa.europa.eu
john.Black@bristowgroup.com
EHEST Secretariat
Michel.Masson@easa.europa.eu
Jeremie.Teahan@easa.europa.eu

## Slide 2: NOTES TO INSTRUCTORS
This presentation is intended for on-site emergency personnel (police, firefighters, ambulance, etc.) requesting or expecting a helicopter in the area
Review and change the presentation in order to fit your training needs
Please refer to the EHEST «Helicopter Mission Request Vade Mecum» document for explanations

## Slide 3: DISCLAIMER
The trainer and the training organisation shall verify the included information and change them accordingly in order to comply with national and local rules and Regulations.

## Slide 4
MISSION REQUEST
Typical scenario
Request a mission
Identifying the area
Prepare the landing area
Receiving the helicopter
Helicopter on ground
What pilots see
The R.O.M.A. checklist
Today’s topics

## Slide 5
TYPICAL SCENARIO

## Slide 6: TYPICAL SCENARIO
TYPICAL SCENARIO
Following an event, somebody will trigger the emergency dispatch centre
Information exchanged at this stage is extremely important

## Slide 7: TYPICAL SCENARIO
HELICOPTER INVOLVEMENT
If deemed appropriate, the dispatch centre will request the helicopter intervention
1
2
3

## Slide 8
MISSION REQUEST

## Slide 9: R.O.M.A. - REQUEST

## Slide 10: MISSION REQUEST
DIFFERENT PERSPECTIVES
Things seen from the ground and from the air can differ significantly
Example: car accident…

## Slide 11
On-site personnel perspective:
  «The helicopter can see us from miles.
  They can’t miss!»

## Slide 12
Main uphill road
Old secondary downhill road
The
pilot
overflies
the
main
road
from
Paternò
to
Adrano
-
Information
was not
accurate
enough

## Slide 13
Old secondary downhill road
ADRANO
Main uphill road
Pilot perspective

## Slide 14
AREA IDENTIFICATION

## Slide 15: R.O.M.A. - REQUEST
REPORT
YOUR POSITION
We are
here!

## Slide 16: AREA IDENTIFICATION
IDENTIFY AND REPORT THE PLACE BY:
  Geographical coordinates
  Social media (Google maps, Whatsapp, etc.)
  City, town
  Road/highway number and distance
  River, bridge, overpasses
  Power lines
  Horizontal, vertical landmarks

## Slide 17: AREA IDENTIFICATION
GEOGRAPHICAL COORDINATES
  It’s the most precise and easiest way for pilots
  Available in most smartphones (get acquainted!)
  KNOW HOW TO READ THEM!

## Slide 18: AREA IDENTIFICATION
GEOGRAPHICAL COORDINATES
  There could be 3 ways to display the coordinates:
  Degrees, minutes, seconds: 37° 37' 47.20" N
  Degrees, decimal minutes: 37° 37.787' N
  Decimal degrees: 37.629778° N
  It is important to read each single symbol (° degrees, ‘ minutes, “ seconds) and dots/commas in the exact order

## Slide 19: R.O.M.A. - REQUEST
THESE COORDINATES INDICATE THE SAME PLACE:
Degrees, minutes, seconds:
37° 37' 47.20" N
14° 49' 54.86" E
Degrees, decimal minutes:
37° 37.787' N
14° 49.914' E
Decimal degrees:
37.629778° N
14.831906° E

## Slide 20: R.O.M.A. - REQUEST
40 Km
1 Km
  Accident site:
  37° 37' 47.20" N 14° 49' 54.86" E
THESE COORDINATES HAVE THE SAME FIGURES, BUT INDICATE WRONG PLACES:
  Wrong coordinates 1:
  37° 37.4720’ N 14° 49.5486’ E
  Wrong coordinates 2:
  37.374720° N 14.495486° E

## Slide 21: AREA IDENTIFICATION
Learn the social opportunities…

## Slide 22
Some possible references…
City park
River tributary
Bridge
N, E, S, W of the city
Road along the river left side bank
High voltage power line
Village (name)
south of city (name), along the left bank of the river

## Slide 23
Some possible references…
Three stores red house
Sport’s field
House under construction
N-S power line
E-W power line

## Slide 24: AREA IDENTIFICATION
NEARBY ALTERNATE LANDING AREAS
  Hospital landing site, civilian heliports, military training sites, big flat fields, sport fields, empty car parking areas, etc.
  Guardian should be contacted for area availability
  Sandy, light soil area should be watered
  Fresh snow should be stepped
  Lights should be switched on well before
  Suitability: entrance width, connecting roads, etc.

## Slide 25: R.O.M.A. - REQUEST

## Slide 26: AREA IDENTIFICATION
PILOTS NEED TO KNOW:
Visibility
Clouds (height and coverage)
Strong wind
Meteorological phenomena

## Slide 27: R.O.M.A. - REQUEST
Local clouds & visibility can be not so obvious…

## Slide 28
ESTIMATE AND REPORT THE LOCAL VISIBILITY
Below 1 km
Between 1 and 3 km
Around 5 km
10 or more km

## Slide 29: AREA IDENTIFICATION
ESTIMATE AND REPORT THE HEIGHT OF THE CLOUDS
  The clouds are just above the houses, trees, constructions
  I can definitely see the clouds moving above my head
  I can see the clouds below/touching/just above the mountain/hill peaks
  The clouds are well above the area/mountains

## Slide 30: R.O.M.A. – METEOROLOGICAL CONDITIONS
I can see clouds just above the light pole…

## Slide 31: R.O.M.A. – METEOROLOGICAL CONDITIONS
I can see clouds just below the mountain peaks…

## Slide 32: R.O.M.A. – METEOROLOGICAL CONDITIONS
I can see clouds above mountain peaks…

## Slide 33: AREA IDENTIFICATION
ESTIMATE AND REPORT THE CLOUD COVERAGE
  I cannot see the sky
  I can barely see the sky
  There are several holes where I can see the sky
  The sky can be seen quite well

## Slide 34: R.O.M.A. – METEOROLOGICAL CONDITIONS
I cannot see the sky…

## Slide 35: R.O.M.A. – METEOROLOGICAL CONDITIONS
I can barely see the sky…

## Slide 36: R.O.M.A. – METEOROLOGICAL CONDITIONS
I can see most of the sky…

## Slide 37: AREA IDENTIFICATION
REPORT ANY METEOROLOGICAL PHENOMENA
  Rain, shower rain, hail, snow
  Tornado, waterspout
  Lightning

## Slide 38: R.O.M.A. – METEOROLOGICAL CONDITIONS
Report any meteorological phenomena
you can see in the vicinity

## Slide 39: AREA IDENTIFICATION
REPORT IF YOU OBSERVE
STRONG OR GUSTING WIND

## Slide 40: R.O.M.A. - REQUEST
A gust of wind can push the helicopter away from the landing site
(Treasure Island – Fiji 23 Dec 2015)

## Slide 41: AREA IDENTIFICATION
REPORT LANDING SITE CONDITIONS & OBSTACLES
  Power lines and major obstacles
  Any dangerous condition (fires, flammable substances, etc.)

## Slide 42: R.O.M.A. - REQUEST
Power lines can be invisible!...
…report them!

## Slide 43
PREPARE THE LANDING AREA

## Slide 44: AREA PREPARATION
WHEN PREPARING THE SITE, PAY ATTENTION TO ALL POTENTIAL OBSTACLES
  A flat, obstacle free, 25 x 25 meters’ open area needed (sometimes 50 x 50 meters)
  Power lines
  No lose objects
  Protruding objects < 50 cm
  Persons
  Properties

## Slide 45: R.O.M.A. - OBSTACLES
PERSONNEL…
keep them away: rotor downwash can rise dangerous objects

## Slide 46: R.O.M.A. - OBSTACLES
STOP THE TRAFFIC
in both directions
Keep vehicles and motorbikes at least
100 m away

## Slide 47: AREA PREPARATION
Tents or tarpaulins
can easily fly away

## Slide 48: R.O.M.A. - OBSTACLES
Ward off pets, cattle, wild animals and birds

## Slide 49
RECEIVING THE HELICOPTER

## Slide 50: RECEIVING THE HELICOPTER
MAKE YOURSELF VISIBLE

## Slide 51: R.O.M.A. - REQUEST
Report any fire in the area
Smoke can be seen well far away
20 NM

## Slide 52
Use handhold flares (preferable)

## Slide 53
Projectile pyrotechnics flares
(try to avoid)

## Slide 54
Use the vehicle flashing lights,
but, remember…
vehicles under bridges or high vegetation are difficult to see from the air

## Slide 55
“We are at your 10 o’clock”
If in contact,
use the “clock position”

## Slide 56
“LAND HERE…”

## Slide 57
Signal the landing site

## Slide 58: RECEIVING THE HELICOPTER
Lose material can be dangerous
for the helicopter and for the nearby persons

## Slide 59
PROTECT
YOURSELF

## Slide 60: R.O.M.A. - OBSTACLES
If you are giving indications over a snowed surface…

## Slide 61
…lean down on one knee
and keep still,
protecting your eyes.
You could be
the only visible reference
for the landing pilot.

## Slide 62
MIND YOUR HAT!

## Slide 63
WINCH OPERATIONS
Keep your position
Do not touch the hook
Protect yourself
Hold on a steady structure
Let winched personnel come to you

## Slide 64
HELICOPTER
ON GROUND

## Slide 65: HELICOPTER ON GROUND

## Slide 66: HELICOPTER ON GROUND
NOTE
Even if familiar…
…do not consider yourself authorized
to approach and work within the helicopter area,
even when the rotor is stopped:
ALWAYS EXPECT AND FOLLOW
THE CREW DIRECTIVES

## Slide 67: HELICOPTER ON GROUND

## Slide 68: HELICOPTER ON GROUND

## Slide 69
TAIL
ROTOR
IS
DANGEROUS

## Slide 70
D A N G E R

## Slide 71
D A N G E R

## Slide 72
D A N G E R

## Slide 73: HELICOPTER ON GROUND
APPROACH AND LEAVE THE AIRCRAFT AT THE LOWEST POINT OF THE TERRAIN

## Slide 74: HELICOPTER ON GROUND
WHEN LOADING OR UNLOADING THE AIRCRAFT, DO NOT THROW OBJECTS CLOSE TO THE HELICOPTER
LONG OBJECTS, LIKE SKIS OR BACKBOARDS, MUST BE CARRIED HORIZONTALLY

## Slide 75
Persons not involved should be kept away

## Slide 76: HELICOPTER ON GROUND
Smoking is prohibited at any time in proximity of the helicopter

## Slide 77
WHAT PILOTS SEE

## Slide 78: WHAT PILOTS SEE
FOLLOWING IS
WHAT A PILOT SEE
ARRIVING IN AN EMERGENCY SITE
AND
WHAT HIS CONSIDERATIONS ARE

## Slide 79
POWER LINE: problems for landing and take-off
Accident
TYPICAL CAR ACCIDENT SCENARIO
LIGHT POLES: problems for landing and take-off

## Slide 80
POWER LINE
Most suitable landing place
- front and back doors open free
AMBULANCES: - free wheeled stretchers
- free sheets on stretchers
PERSONS NOT INVOLVED: walking free, close to landing site
TRAFFIC SIGN: close to the landing site
TRAFFIC IN OPPOSITE WAY: not stopped

## Slide 81
ALTERNATE
LANDING
SITES
ALTERNATE
LANDING
SITES
Traffic has not been stopped
Bushes and guardrail hamper the patient transfer
ALTERNATE
LANDING
SITES
Slopped surface
Trees and bushes
Obstacles
Traffic

## Slide 82
DID YOU SPOT ALL THESE ELEMENTS?

## Slide 83
THE
R.O.M.A.
CHECKLIST

## Slide 84: R.O.M.A. CHECKLIST
Dispatch centre and on-site personnel exchange information
On-site personnel verify and prepare the landing site
Dispatch centre passes information to pilot
Helicopter flies faster and safer
to the emergency site
R.O.M.A.
R.O.M.A.

## Slide 85
R. – Request
  Pass all the important information
O. – Obstacles
  Verify and report the potentially dangerous obstacles
M. – Meteorological
  Report the metrological conditions in the area
A. – Area preparation
  Prepare the area and verify safety

## Slide 86: https://easa.europa.eu/essi/ehest/ ehest@easa.europa.eu
QUESTIONS?