## Slide 1: Internal/External inspections (in MSG-3)
Prepared by:
Luca Tosini
Aircraft Maintenance Expert
EASA Aircraft Maintenance & CAMO Section (FS.1.2)
Date: 28/04/2025

## Slide 2
Internal/External inspections
MSG-3 mentions internal/external
  “Other Structure is that which is judged not to be a Structural Significant Item. It is defined both externally and internally within zonal boundaries.”
  “The following procedures may be used a. Divide the aircraft externally and internally into zones”
MSG-3 however does not define “internal” or “external”
Issue is twofold
  Information required to perform analysis (e.g. information to develop PPH procedures)
  Information required to perform the task (information to the mechanic/inspector)
Some PPH include a customized definition
Other PPH without any definition
  Some Maintenance programs identify if the task is internal or external, but it is not standard practice

## Slide 3
Existing MRBR Examples
Internal/External clearly identified
Internal/External not clearly/explicitly/systematically identified

## Slide 4
Existing Analysis Examples
MSG-2
Same rating gives different Interval
for External/Internal SSI
Same Interval for External/Internal SSI

## Slide 5
Questions
Should MSG-3 or IMPS introduce an harmonized definition for “Internal” and “External” (analysis and inspections) ?
Impact on MRBR Development?
Manufacturers
Impact on Maintenance Programs?
Operators

## Slide 6: Thank you!