## Slide 1
May 5-9th, 2025
IMRB PB, Dubai
Hosted by UAE GCAA
Rotorcraft Maintenance Programs Industry Group (RMPIG) update
International MRB Policy Board Meeting
Notes: 0

## Slide 2
Overview
Current leadership:
  Chair: Giacomo Gibilisco (Leonardo)
  Vice-Chair: Frederic Reynaud (Airbus Helicopter)
  Vice-Chair deputee: Jeremy Burgess (Bell)
  Secretary: Gordon Bruce (Fokker)
RMPIG Action Items:
  No currently OPEN Action Items

## Slide 3
Latest Meeting and Activities Summary
    RMPIG activities
  RMPIG held in the last year
July 15, 2024 Dec 10, 2024 Jan 31, 2025 | Feb – March, joint with MPIG July 13, 2025 (planned)
  CIP 2025-02 IP44 application in rotorcrafts based on IAM 2024 technical topic
  Provide an RMPIG position on CIP content developed in MPIG with Vol.02 affected
  Provide support in the SW for harmonization of SSI definition among V.01 and V.02
  Increased participation into MSG-4 multiple WG

## Slide 4
Notes: 3

## Slide 5
May 5-9th, 2025
IMRB PB, Dubai
Hosted by UAE GCAA
Adverse Effect on Safety – Harmonization
Material for future CIP
Notes: 4

## Slide 6: SSI definition harmonization – CIP EASA in 2025
  Vol.01
  Vol.02
  Guessed outcome (from SWG presentation Jan 2025)
  Vol.01 + Note
In IAM 2025 update of the SSI definition has been discussed on the base of EASA CIP proposal reviewed with SWG support adopting the same approach considered for IP192 (Single Definition + Note to consider additional item to be analyzed as SSI).
A Structural Significant Item (SSI) is any detail, element or assembly, which contributes significantly to carrying flight, ground, pressure or control loads, and whose failure could affect the structural integrity necessary for the safety of the aircraft.
A Structural Significant Item (SSI) is any detail, element or assembly, which contributes
significantly to carrying flight, ground, pressure or control loads or external load, and
whose failure could affect the structural integrity necessary for the safety of the aircraft
and/or might cause serious or fatal injury to human occupants.
Considerations, as SSI should be given to:.
structural components of a system whose function includes human external cargo (HEC) carrying and whose failure might cause serious of fatal injury to HEC, through coordination between System and Structures WG in accordance with established transfer policies and procedures."

## Slide 7: Adverse Effect on Safety – Original difference (IP147)
SSI Definition amendment align “half” of the IP 147 original issue in respect to the SSI.
Other “half” issue for MSI was solved in IP147 changing the definition of “Adverse effect on safety” in respect to the SSI selection with definition modified as follows:
This last change had also a benefit towards MSI analysis of HEC related system when dealing with answers to questions of the PowerPlant section analysis in Vol.02.

## Slide 8: Adverse Effect on Safety – EASA Roadmap (Haikou 2024)
  RESOLUTION of the difference is possible following indication proposed by EASA presented in IAM 2024 within the Roadmap for SSI definition Technical Topic
  When proposing as slide 7 to include a definition of Human Occupant

## Slide 9: Adverse Effect on Safety – Human Occupant definition
  Term Human Occupant is already common in Vol.01 and 02 and used into “Adverse Effect on safety” definition and can be defined to include the different part related to “external” crew members.
  *Human occupant: any person occupying/boarding/disembarking the aircraft during operation, including those supported externally by an aircraft system or structure (e.g. personnel-carrying device system), if applicable.
  *Definition here proposed as per EASA Roadmap suggestion in PPT
MSG-3 Vol 1, glossary
MSG-3 Vol 2, glossary

## Slide 10: MSG-3 impacts for Human Occupants definition
The above definition agreement would produce the following (minimum) effects on Vol.01 and Vol.02.
Vol.01 | Vol.02
Glossary – Add definition of Human Occupants in | 
N/A | Glossary – Modify definition to aligned back common to Vol.01 Adverse Effect on Safety: Safety shall be considered as adversely affected if the consequences of the failure condition would prevent the continued safe flight and landing of the aircraft and/or might cause serious or fatal injury to human occupants, including those directly supported by external load carrying systems (i.e. hoist/cargo hook etc.)
N/A | Section 2-3-5.2 Direct adverse effect on safety [Same wording as above]

## Slide 11
Notes: 10