## Slide 1
May 5, 2025
CIP MPIG 2023-01 Rev. 3– Use of other applicable and effective tools for visual inspections
Notes: 0

## Slide 2
Background
MPIG understood the PB feedback as follows:
    The PB supports a standardized approach for the introduction of other/new “visual aids”
    Analysis of applicable and effective tooling meeting the task intent should occur at the WG level
    Other visual aids may satisfy the task’s intent, improve safety, access, and efficiency
    Initial application should be focused on Zonal GVI

## Slide 3
Sub-Team considerations
The WG‘s methodology should consider currently available tools that are applicable and effective in meeting a GVI‘s task‘s intent
Amend MSG-3‘s visual inspection (GVI) language
Introduce IMPS guidance addressing validation and related criteria in the PPH:
  Confirm task intent is met with applied methods and tooling
  Define related limitations (e.g., Zonal GVI)
Innovation is providing technicians/inspectors with more readily available tools that are safer, more effective, and efficient than a mirror and a flashlight for image capturing
  Cell phone cameras, power-controlled devices with cameras
MSG-3 is not keeping up with these tooling innovations

## Slide 4
Proposed IMPS revision
A. Revise IMPS 3.7 to add guidance for the TCH to consider the use of industry standard tools in the task validation process.
  3.7 The type certificate holder has the responsibility to develop is responsible for developing a methodology to validate the maintenance procedures written to support the completion of supporting MRBR tasks. The objective of the this validation is to ensure the maintenance procedure can be performed and that the intent of the MRBR task is also complied withmet. The validation includes any methods or tooling deemed applicable and effective by the MSG-3 analysis. The results of the validation shall be made available to the CA or VA upon request. If task validation reveals finds that the intent of the MRB task cannot be met, this should be reported be fed back to the ISC. They should for review and correction of any errors in the analysis. for possible errors and correct as required.
Note: Other edits are grammatical corrections evident and fixed

## Slide 5
Proposed IMPS revision
  continued: Revise IMPS Section 3.7
  3.7.1 The TCH will identify the applicable and effective tools for the working group to consider in meeting the task's intent. The PPH may include additional criteria, conditions, and/or limitations related to tool usage as appropriate. This could involve categorizing some tools as optional and defining limits on their scope of application (e.g., zonal GVI for optional image-capturing devices) as agreed upon by the TCH and the certifying authority.

## Slide 6
Proposed IMPS revision
  continued: Revise IMPS Section 3.7
  PPH example on 3.7.1: The PPH may clarify that the use of powered digital image capture devices is optional to complete a GVI, and if used, it is limited to zonal GVIs
  When powered digital image capture devices are being used to meet the intent of a GVI, the PPH will direct the requirement for task validation as appropriate to the MRB.

## Slide 7
Proposed MSG-3 revision
B. Amend MSG-3 Chapter 2-1-2 as follows:
  3. Method for Scheduled Maintenance Development
  …This information (e.g. task purpose, accesses, tools/GSE, main steps of the procedure, estimated elapsed time/labor hour, pass/fail criteria ...) will be recorded in the MSG-3 analysis or referenced supporting documentation for tracking purposes. During task selection, working groups should evaluate the applicability and effectiveness of aerospace tooling (e.g., image capturing devices) capable of meeting the task’s intent

## Slide 8
Proposed MSG-3 revision
  Amend the glossary definition for “Inspection – General Visual (GVI) as follows: A visual examination of an interior or exterior area, installation or assembly to detect obvious damage, failure or irregularity. This level of inspection is made from within touching distance unless otherwise specified. A visual aid (e.g. mirror or image capturing device) may be necessary appropriate to enhance visual access to all exposed surfaces in the inspection area. This level of inspection is made under normally available lighting conditions such as daylight, hangar lighting, flashlight or drop-light and may require removal or opening of access panels or doors. Stands, ladders or platforms may be required to gain proximity to the area being checked. Basic cleaning may be required to ensure appropriate visibility.

## Slide 9
Summary Conclusion
Policy Board feedback | Recommended action
The PB supports a standardized approach for the introduction of other/new “visual aids” | Proposed a standardized approach
The analysis of applicable and effective tooling meeting the task intent should occur at the WG level | Proposed new text in Chapter 2-1-2 to define that working groups should evaluate applicable and effective tooling that meets the task’s intent. Proposed IMPS 3.7 content that emphasizes validation should include any methods or tooling deemed applicable and effective by the MSG-3 analysis, plus other grammatical clean up

## Slide 10
Summary Conclusion
Policy Board feedback | Recommended action
Other visual aids may satisfy the task’s intent, improve safety, access, and efficiency | Proposed a minor MSG-3 glossary change to: Inspection – General Visual (GVI) to introduce …A visual aid (e.g., mirror, image capturing device) may be necessary appropriate to enhance…
Initial application should be focused on Zonal GVI | Introduced new 3.7.1 IMPS guidance for the PPH to other conditions or criteria such as: Tooling limitations (e.g., Zonal GVI) requiring CA approval Annotate if any tools considered are optional

## Slide 11
Question, comments?
Notes: 10