## Slide 1
IAM 2025
CIP RMPIG 2025-02 Clarification of IP44 definition in IMPS
Presented by: F. Reynaud (Airbus Helicopters)
Notes: 0

## Slide 2
Clarification of IP44 definition in IMPS
1/ Issue:
IP44 guideline is defined as not exhaustive in IMPS and shall be utilized as the basis for OEM procedure.
This definition leaves a room open for interpretation of what can be used in addition to this guideline.
2/ Problem:
IP44 Guidelines allows complementary Data / Analysis to be used in addition to standard analysis.
The following examples illustrates what OEM needs to manage:
Data collected from operators can be not enough accurate to allow OEM to assess significance of findings. In that case, OEM can provide additional Data/Analysis to assess significance of findings.
Sample representativeness could be more difficult to reach on Rotorcraft due to Fleet size and yearly flight rates. In that case, OEM can propose to perform deep investigations with a reduced size of the sample compensated by improving the quality of reports done for each task application (example: investigation performed by OEM to ensure that level of damages is at expected level to extend the interval). In this case, OEM must guarantee a level of safety management equivalent to the statistical approach. Representativeness of sample must be managed and be conservative (Missions, Geographical environments, …)
This complementary data/analysis (e.g. accurate investigation results, significance of findings assessment, test results) should be implemented in addition to IP44 requirements and must not replace them.

## Slide 3
Clarification of IP44 definition in IMPS
3/ Recommendation
IMPS definition: While this guidance is not intended to be exhaustive, it shall be utilized as the basis for a Policy and Procedures Handbook (PPH) procedure when the OEM/TCH, MRB, and ISC wish to proceed with evolution / optimization regarding the MRBR process.
Industry understanding: To complete analysis, additional data may be used to support the substantiation, as far as their use is described and approved in a PPH.

## Slide 4
THANK YOU