## Slide 1: Functions inside “smart” LRUs
Prepared by:
Luca Tosini
Aircraft Maintenance Expert
EASA Aircraft Maintenance & CAMO Section (FS.1.2)
Date: 28/04/2025

## Slide 2: Introduction
MSG-3 2022.1

## Slide 3: Introduction
This defines the lower boundary to select the highest manageable level of analysis.
Today more and more on-aircraft replaceable components (Line replaceable Units, LRU) are “smart” and provide several functions comparable to the system level function of traditional systems.
The MSG-3 logic seems not suited to analyse such functions.

## Slide 4: Traditional vs. Smart
Traditionally, systems were composed of LRUs having a simple inner design, that typically just performed one single function.
Example: traditional battery overview
according to ATA iSpec 2200 typically an LRU within the 24-30 “DC Generation” sub-system.
composed by passive components like cells, bars, housing, padding and connectors (the external connector only provided two pins).
more sophisticated batteries may have temperature sensor(s) included and an according additional connector.
the only components inside that are serviceable are the cells, their maintenance is typically part of scheduled task.
All additional functions required at aircraft level (battery switching, charge control, voltage indication, current indication, temperature indication, overvoltage protection, overcurrent protection, temperature protection, ventilation etc.) was provided by the aircraft systems and analysed in the according MSIs with support of the manufacturer in full knowledge of the system design.

## Slide 5: Traditional vs. Smart
Nowadays more and more complex LRUs are installed on aircrafts/rotorcrafts
  “smart” LRUs, that actually constitute at least a sub-system, if not an entire system, of their own, providing several functions that previously were provided at system level.
Example: modern battery functions overview (do constitute a full DC system per-se)
Battery switching
current limitation
single faulty cell isolation
(automatic) cell heating
cell balancing
under- and overtemperature protection
under- and overcharge protection,
under- and overcurrent protection
under- and overvoltage protection
condition monitoring
capacity information
state-of-charge information
capacity and charge indication (on the housing)
test capability
digital communication for maintenance purpose
software programming of functions.

## Slide 6: Traditional vs. Smart
Modern batteries provide a long list of functions previously provided by aircraft systems, and test and monitoring capability previously provided by maintenance shops.
Additionally those modern components may provide functions that in the past were not possible to be provided by the aircraft systems: these batteries do communicate with aircraft systems and test equipment with analogue signals and digital interfaces.
These batteries can take autonomous decisions like isolating the battery from the DC bus leaving the bus unpowered with no way for the pilot to influence this.
Many functions are software driven and can be updated requiring configuration control to ensure that the MSI analysis remains in line with the actually installed software capabilities and behavior of the components.

## Slide 7: Possible several issues*
It may not be easy to identify all aircraft level functions that are performed by the smart LRU, it will especially hinder the identification of all failure causes.
The successful performance of certain functions of the smart LRU (e.g. an overtemperature protection) may at aircraft level constitute a Functional Failure (battery disconnects from the aircraft, no more backup DC power for essential equipment).
When developing the ICA for the unit, the battery manufacturer can not evaluate failure effects at aircraft level as this requires detailed knowledge about the specific aircrafts DC or even electrical system architecture. Therefore the data available to the aircraft manufacturer cannot be considered as comprehensive.
As the unit contains user loadable software and the possibility to deactivate certain functions and to set certain performance parameters, configuration control for installation but also for data analysis during maintenance may become an issue at MSG-3 analysis level.
  *NOTE: specifically worded for batteries, but general in nature

## Slide 8: Conclusion
The MSG-3 logic seems not suited to analyse such smart components, especially when highly integrated in the aircraft/rotorcraft system design.
As a first step, in the breakdown of the aircraft/rotorcraft systems, the TCH should identify those on-aircraft replaceable / line replaceable components, that in the sense of MSG-3 or ATA iSpec2200/S1000D do constitute sub-systems or systems on their own.
A “smart” component may have to be selected as an MSI if it is so complex, that only at that level all Functions, Functional Failures and Failure Causes can be covered.
If analysis below LRU level is required, support by the vendor needs to be ensured by the TCH, either by providing detailed enough description documents or by having vendor experts being involved in the analysis and the Working Group(s).
Comments?

## Slide 9: Thank you!