## Slide 1
March 27, 2025
MPIG – Other Topics
Notes: 0

## Slide 2
MPIG – Other Topics
Escape Slide Sampling
Instructions for Continued Airworthiness (ICA) availability at Entering in Service

## Slide 3
MPIG – Other Topics
Escape Slide Sampling

## Slide 4
MPIG – Escape Slide Sampling
For US operators, a FAA ‘National Requirement’ exists which requests an operational check of the cabin escape slides/raft on a sampling basis. For further details refer to AC 43-208.
c. Why Are Maintenance Time Limitations Needed?
(1) Inspection periods for EES will determine the continued serviceability and immediate readiness of EES equipment for its intended emergency purpose. …….
(2) Two types of inspection tasks are used in aircraft maintenance: failure-finding tasks, which identify functional failures, and failure prevention tasks, which identify potential failures. ……
(3) Scheduled deployments on the aircraft or during a combination of on-aircraft functional tests, inspections, and test-fixture usage may be used, provided the test-fixture replicates the aircraft installation. The number of scheduled deployment checks should be included for statistical validity. Inadvertent deployments, while a source of useful information, should not be considered or used as the sole source of reliability information.

## Slide 5
MPIG – Escape Slide Sampling
There is no AC 43-208 equivalent in the EASA world.
Airbus has an OPC of Escape Slide in all its MRBRs
This is a sampling of slide deployment each door type synchronized with the overhaul interval
Sampling is done on fleet level not individual MSN
It is not an applicable and effective task in regards to MSG-3
Do we need a CIP to address this subject?

## Slide 6
MPIG – Other Topics
Instructions for Continued Airworthiness (ICA) availability at Entering in Service

## Slide 7
MPIG – EASA Part 21 ICA availability 100%
Background
Design approval applicants/holders need to prepare Instructions for Continued Airworthiness (ICA) for the operators/owners as part of the obligations set in 21.A.44, 21.A.109, 21.A.118A and 21.A.451.
21.A.61(a), 21.A.107 and 21.A.120A(a) allow to delay the furnishing of certain parts of the ICA to the operator/owner and any other person required to comply with any of those instructions until EIS or, for 21.A.61(a) and 21.A.120A(a), even beyond EIS for items dealing with overhaul or other forms of heavy maintenance.
In addition, ICA are required to demonstrate compliance with the certification basis as part of the design approval according to 21.A.21, 21.A.103, 21.A.115 and 21.A.437. Furthermore, the approved airworthiness limitation section (ALS) is part of the type design in accordance to 21.A.31.
This means, on one hand, ICA may be delayed until EIS or even beyond, but, on the other hand, the Agency must be satisfied, that sufficient ICA are available at the time of design approval and the remaining ICA will subsequently be provided.
Source: EASA Certification Memo CM-ICA-001 Iss. 1

## Slide 8
MPIG – EASA Part 21 ICA availability 100%
a type-certificate or restricted type-certificate to each known owner of one or more products upon its delivery or upon the issuance of the first certificate of airworthiness or restricted certificate of airworthiness for the affected aircraft, whichever occurs later,
(c) By way of derogation from point (b), the type-certificate holder or restricted type-certificate holder may delay the availability of a part of the instructions for continued airworthiness, dealing with long lead accomplishment instructions of a scheduled nature, until after the product or modified product has entered into service, but shall make those instructions available before the use of this data is required for the product or modified product.
Delayed availability option does not exist in FAR21.50 (b)

## Slide 9
MPIG – EASA Part 21 ICA availability 100%
21.50 Instructions for continued airworthiness and manufacturer's maintenance manuals having airworthiness limitations sections.
(a) The holder of a type certificate for a rotorcraft for which a Rotorcraft Maintenance Manual containing an “Airworthiness Limitations” section has been issued under § 27.1529 (a)(2) or § 29.1529 (a)(2) of this chapter, and who obtains approval of changes to any replacement time, inspection interval, or related procedure in that section of the manual, must make those changes available upon request to any operator of the same type of rotorcraft.
(b) The holder of a design approval, including either a type certificate or supplemental type certificate for an aircraft, aircraft engine, or propeller for which application was made after January 28, 1981, must furnish at least one set of complete Instructions for Continued Airworthiness to the owner of each type aircraft, aircraft engine, or propeller upon its delivery, or upon issuance of the first standard airworthiness certificate for the affected aircraft, whichever occurs later. The Instructions for Continued Airworthiness must be prepared in accordance with §§ 23.1529, 25.1529, 25.1729, 27.1529, 29.1529, 31.82, 33.4, 35.4, or part 26 of this subchapter, or as specified in the applicable airworthiness criteria for special classes of aircraft defined in § 21.17(b), as applicable. If the holder of a design approval chooses to designate parts as commercial, it must include in the Instructions for Continued Airworthiness a list of commercial parts submitted in accordance with the provisions of paragraph (c) of this section. Thereafter, the holder of a design approval must make those instructions available to any other person required by this chapter to comply with any of the terms of those instructions. In addition, changes to the Instructions for Continued Airworthiness shall be made available to any person required by this chapter to comply with any of those instructions.
Source: https://www.ecfr.gov/current/title-14/chapter-I/subchapter-C/part-21/subpart-B/section-21.50

## Slide 10
MPIG – EASA Part 21 ICA availability 100%
ISSUES
  The approval and EIS of design changes (modifications) with impact on ICAs, MRBR in particular, may not fit to the MRBR revision cycle and through this might not be available at EIS.
  As per the MRB Process, changes to the MRBR are requiring Working Group and Industry Steering Committee review/validation prior MRB approval, consequently MRBR changes having a long lead time.
  IMPS Chapter 4.6.6 is providing the opportunity to publish Temporary Revision (TR) to the MRBR. However, IMPS is pointing out that TRs are only to be used on an exceptional basis.
Do we need a CIP to get the use of TRs changed?
Do we what to review the MRBR approval process?

## Slide 11
Notes: 10